## Slide 1: MP-2 PROJECT Digital circuit optimization via geometric programming
Priyansu Panda -2010030324
Jonallagada Krishna sai Roshith-2010030283
Harshitih Naidu -2010030515
Sai Hitesh -2010030510

## Slide 2: INTRODUCTION
The complexity of digital integrated circuits (ICs) has been increasing exponentially since around 1960, with the number of components or devices in a single IC more than doubling every 18 months. Some current ICs contain over 100 million devices and a similar number of wires connecting them. The design of such complex ICs relies heavily on electronic design automation (EDA) and computer-aided design (CAD) technologies. we focus on just one step in the design of a digital circuit: the selection of appropriate sizes for the devices, gates, and wires. These sizes can correspond to physical dimensions such as the width of a transistor channel or wire segment, or to more abstract parameters like the drive strength of a gate (which is closely related to the physical size of the gate). We will also consider extensions in which other design variables, such as threshold and power supply voltage, are also selected. The choice of these design variables can have a strong influence on the three primary top level objectives: the total area of the circuit, the total power it consumes, and the speed at which it can operate.

## Slide 3: ABSTRACT
A method for digital circuit optimization based on formulating the problem as a geometric program (GP) or generalized geometric program (GGP), which can be transformed to a convex optimization problem and then very efficiently solved. We start with a basic gate scaling problem, with delay modeled as a simple resistor-capacitor (RC) time constant, and then add various layers of complexity and modeling accuracy, such as accounting for differing signal fall and rise times, and the effects of signal transition times. We then consider more complex formulations such as robust design over corners, multimode design, statistical design, and problems in which threshold and power supply voltage are also variables to be chosen. Finally, we look at the detailed design of gates and interconnect wires, again using a formulation that is compatible with GP or GGP. Subject classifications: programming: geometric; engineering: computer-aided design; digital circuit optimization.

## Slide 4: APPLICATIONS
1. we can solve even large GPs very effectively, using recently developed methods.
2. so once we have a GP formulation, we can solve circuit design problem effectively.
The reason we of using it-
1. GP is especially good at handling a large number of concurrent constraints. 2. GP formulation is useful even when it is approximate

## Slide 5: SOFTWARE REQUIRED
PyCharm Community Version
Python 3.10
Jupyter Notebook

## Slide 6: APPROACH
Most problems don't come naturally in GP form; be prepared to reformulate and/or approximate.
GP modeling is not a "try my software" method; it requires thinking.
Our Approach:
Start with simple analytical models (RC, square-law, Pelgrom,...) to verify GP might apply.
Then fit GP-compatible models to simulation or measured data.
For highest accuracy, revert to local method for final polishing.

## Slide 7: CONCLUSION
• Comes up in a variety of circuit sizing contexts.
Can be used to formulate a variety of problems.
Admits fast, reliable solution of large-scale problems
Is good at concurrently balancing lots of coupled constraints and objectives.
Is useful even when problem has discrete constraints.

## Slide 8
THANK YOU!!!